## Slide 1
Differences between similar building blocks
CEOS-ARD Product Family Specifications — current wording per PFS and alignment proposals from the review feedback

## Slide 2
Contents (1/2)
Requirement | AR | NLSR | SR | ST | CB | GSLC | INSAR | NRB | ORB | POL
corrections/atmosphere-* |  | ✓ |  | ✓ |  |  |  |  |  | 
Directional Atmospheric Scattering | ✓ |  | ✓ |  |  |  |  |  |  | 
Geometric Correction | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 
Ozone Corrections | ✓ |  | ✓ |  |  |  |  |  |  | 
Water Vapour Corrections | ✓ |  | ✓ |  |  |  |  |  |  | 
Measurement Normalisation | ✓ | ✓ | ✓ |  |  |  |  |  |  | 
Measurement Uncertainty | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 
Algorithms | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 
Auxiliary Data | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
metadata/crs-* | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
metadata/data-access-* | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
metadata/geo-area-* | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Geometric Correction Methods | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 
Instrument | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Metadata Machine Readability | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Map Projection | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 

## Slide 3
Contents (2/2)
Requirement | AR | NLSR | SR | ST | CB | GSLC | INSAR | NRB | ORB | POL
Processing Chain Provenance | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 
Radiometric Accuracy |  | ✓ | ✓ |  | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Sensor Calibration | ✓ | ✓ | ✓ | ✓ |  | ✓ | ✓ | ✓ | ✓ | ✓
Spectral Bands | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 
metadata/time-* | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
metadata/traceability-* | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Cloud | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 
Cloud Shadow | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 
per-pixel/incomplete-testing-* | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 
per-pixel/land-water-* | ✓ | ✓ | ✓ |  |  |  |  |  |  | 
No Data | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 
Saturation | ✓ | ✓ | ✓ | ✓ |  |  |  |  |  | 
Snow/Ice Mask |  | ✓ | ✓ |  |  |  |  |  |  | 
Terrain Occlusion |  | ✓ | ✓ | ✓ |  |  |  |  |  | 
Solar and Viewing Geometry | ✓ |  | ✓ | ✓ |  |  |  |  |  | 
DOIs / DOIs | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓

## Slide 4
Scope
Building blocks that exist in several variants (e.g. time-ar/-sar/-sr/-st) are compared; only the differences are shown — fields that are identical across all variants of a group are omitted.
  This is just a first step to get some initial alignment, more steps are likely needed.
The groups are split by the type of the PFS that use them: used by both SAR and Optical PFS, or used only by Optical PFS.
Building blocks used only by SAR PFS are omitted (as are PFS overrides that only affect them): their differences are intentional, as the SAR PFS were a combined document before being split.
Compared fields: title, description, and per requirement level (threshold/goal/image) the description, the optional flag, and the notes.
Ignored fields: id, dependencies, glossary, references, changes, history, remarks.
Not compared: the measurement/measurand/backscatter/… building blocks (intentionally different per product).

## Slide 5
How to read the tables
One slide per building block group. For every field that differs between the variants, a table shows the current text per PFS and the proposed alignment.
Current column — differences to the row marked (baseline) are highlighted:
red struck-through text only appears in the baseline variant
green text only appears in this variant
blue passages are shared with the baseline — used where texts are too different for a diff
(not set) = the field or the whole requirement level is absent in that file
Proposed column — proposed changes relative to the row's current text:
red struck-through text is removed, green text is added by the proposal
(keep as is) = unchanged (explicitly kept or nothing proposed)
DELETE NOTE = proposed removal
gray italic text = proposal that could not be interpreted automatically, shown verbatim
Internal notes are shown below the tables; the raw proposal text is in the slide's speaker notes.

## Slide 6
corrections/atmosphere-* (NLSR, ST)
PFS | Current Title | Proposed Title
ST (baseline) | Corrections for Atmosphere | Atmospheric Corrections (see notes)
NLSR | Atmospheric Corrections | (keep as is)
PFS | Current Threshold Description | Proposed Threshold Description
ST (baseline) | Retrieval methods for estimating surface temperature are provided. | (keep as is)
NLSR | Corrections are applied for atmospheric scattering. Metadata contains a single DOI landing page with references to: - a citable peer-reviewed algorithm - technical documentation regarding the implementation of that algorithm - the sources of ancillary data used to make corrections | Corrections are applied for atmospheric scattering.
PFS | Current Threshold Notes | Proposed Threshold Notes
ST | (no notes) | (keep as is)
NLSR (baseline) | Examples of technical documentation include an Algorithm Theoretical Basis Document, product user guide, etc. | DELETE NOTE
Internal notes: For DOI related discussions see "DOIs" slide.
The two requirements intentionally(?) differ in content (ST: surface temperature retrieval methods; NLSR: atmospheric scattering) and may stay separate; we may want to choose distinct titles if the requirements do different things.
Notes: PROPOSAL:
**Title (ST)**:
```
Atmospheric Corrections
```
**Threshold — description (NLSR)**:
```
Corrections are applied for atmospheric scattering.
```
**Threshold — notes (NLSR)**: Remove
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.
The two requirements intentionally differ in content (ST: surface temperature retrieval methods; NLSR: atmospheric scattering) and stay separate; only the title and the boilerplate are aligned.

## Slide 7
Directional Atmospheric Scattering (AR, SR)
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | Specification of corrections applied for molecular (Rayleigh) scattering and for aerosol scattering and absorption.. | Specification of corrections applied for molecular (Rayleigh) scattering and for aerosol scattering and absorption..
SR | Corrections are applied for aerosols and molecular (Rayleigh) scattering. Metadata contains a single DOI landing page with references to: - a citable peer-reviewed algorithm - technical documentation regarding the implementation of that algorithm - the sources of ancillary data used to make corrections | Specification of corrections applied for molecular (Rayleigh) scattering and for aerosol scattering and absorption.
PFS | Current Threshold Notes | Proposed Threshold Notes
AR (baseline) | See @mobley2016. | (keep as is)
SR | Examples of technical documentation include an Algorithm Theoretical Basis Document, product user guide, etc. | DELETE NOTE
Internal notes: For DOI related discussions see "DOIs" slide.
Notes: PROPOSAL:
**Threshold — description (AR, SR)**:
```
Specification of corrections applied for molecular (Rayleigh) scattering and for aerosol scattering and absorption.
```
**Threshold — notes (SR)**: Remove
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.

## Slide 8
Geometric Correction (AR, NLSR, SR, ST)
PFS | Current Description | Proposed Description
AR (baseline) | Applies for: 1. land 2. inland waters where an independent terrestrial referencing system is available | (keep as is)
NLSR, SR | (not set) | (keep as is)
ST | (not set) | (keep as is)

## Slide 9
Geometric Correction (AR, NLSR, SR, ST) (cont.)
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | Sub-pixel uncertainty is achieved in relative geolocation, that is, the pixels from the same instrument and platform are consistently located, and are thus comparable, through time. Sub-pixel uncertainty is taken to be less than or equal to 0.5-pixel radial root mean square error (rRMSE) or equivalent in Circular Error Probability (CEP) relative to a defined reference image. A consistent gridding/sampling frame is used, including common cell size, origin, and nominal sample point location within the cell (centre, ll, ur). Relevant metadata must be provided under [@geometric-uncertainty] and [@instrument]. | Sub-pixel uncertainty is achieved in relative geolocation, that is, the pixels from the same instrument and platform are consistently located, and are thus comparable, through time. Sub-pixel uncertainty is taken to be less than or equal to 0.5-pixel radial root mean square error (rRMSE) or equivalent in Circular Error Probability (CEP) relative to a defined reference image. A consistent gridding/sampling frame is used, including common cell size, origin, and nominal sample point location within the cell (centre, ll, ur). Relevant metadata must be provided under [@geometric-uncertainty] and [@instrument].
NLSR, SR | Sub-pixel uncertaintaccuracy is achieved in relative geolocation, that is, the pixels from the same instrument and platform are consistently located, and are thus comparable, through time. Sub-pixel uncertaintaccuracy is taken to be less than or equal to 0.5- pixel radial root mean square error (rRMSE) or equivalent in Circular Error Probability (CEP) relative to a defined reference image. A consistent gridding/sampling frame is used, including common cell size, origin, and nominal sample point location within the cell (centre, ll, ur). Relevant metadata must be provided under [@geometric-uncertaintaccuracy] and [@instrument]. | Sub-pixel accuracuncertainty is achieved in relative geolocation, that is, the pixels from the same instrument and platform are consistently located, and are thus comparable, through time. Sub-pixel accuracuncertainty is taken to be less than or equal to 0.5 -pixel radial root mean square error (rRMSE) or equivalent in Circular Error Probability (CEP) relative to a defined reference image. A consistent gridding/sampling frame is used, including common cell size, origin, and nominal sample point location within the cell (centre, ll, ur). Relevant metadata must be provided under [@geometric-accuracuncertainty] and [@instrument].
ST | Sub-pixel uncertaintaccuracy is achieved in relative geolocation, that is, the pixels from the same instrument and platform are consistently located, and are thus comparable, through time. Sub-pixel uncertaintaccuracy is taken to be less than or equal to 0.5- pixel radial root mean square error (rRMSE) or equivalent in Circular Error Probability (CEP) relative to a defined reference image. A consistent gridding/sampling frame is used, including common cell size, origin, and nominal sample point location within the cell (centre, ll, ur)necessary to meet this requirement. Relevant metadata must be provided under [@geometric-uncertainty] and [@instrument]. | Sub-pixel accuracuncertainty is achieved in relative geolocation, that is, the pixels from the same instrument and platform are consistently located, and are thus comparable, through time. Sub-pixel accuracuncertainty is taken to be less than or equal to 0.5 -pixel radial root mean square error (rRMSE) or equivalent in Circular Error Probability (CEP) relative to a defined reference image. A consistent gridding/sampling frame is necessary to meet this requirementused, including common cell size, origin, and nominal sample point location within the cell (centre, ll, ur). Relevant metadata must be provided under [@geometric-uncertainty] and [@instrument].

## Slide 10
Geometric Correction (AR, NLSR, SR, ST) (cont.)
PFS | Current Threshold Notes | Proposed Threshold Notes
AR | 1. The threshold level will not necessarily enable interoperability between data from **different** sources as the geometric corrections for each of the sources may differ. 2. It is useful to note if the sensor is used at its native resolution before geometric correction or that some resampling must be done. | 1. The threshold level will not necessarily enable interoperability between data from **different**different sources as the geometric corrections for each of the sources may differ. 2. It is useful to note if the sensor is used at its native resolution before geometric correction or that some resampling must be done.
NLSR, SR (baseline) | The threshold level will not necessarily enable interoperability between data from **different** sources as the geometric corrections for each of the sources may differ. | 1. The threshold level will not necessarily enable interoperability between data from **different**different sources as the geometric corrections for each of the sources may differ. 2. It is useful to note if the sensor is used at its native resolution before geometric correction or that some resampling must be done.
ST | The threshold level will not necessarily enable interoperability between data from **different** sources as the geometric corrections for each of the sources may differ. | 1. The threshold level will not necessarily enable interoperability between data from **different**different sources as the geometric corrections for each of the sources may differ. 2. It is useful to note if the sensor is used at its native resolution before geometric correction or that some resampling must be done.

## Slide 11
Geometric Correction (AR, NLSR, SR, ST) (cont.)
PFS | Current Goal Description | Proposed Goal Description
AR (baseline) | Sub-pixel uncertainty is achieved relative to an identified absolute independent terrestrial referencing system (such as a national map grid). Relevant metadata must be provided under [@geometric-uncertainty] and [@instrument]. | (keep as is)
NLSR, SR | Sub-pixel uncertaintaccuracy is achieved relative to an identified absolute independent terrestrial referencing system (such as a national map grid). A consistent gridding/sampling frame is necessary to meet this requirement. Relevant metadata must be provided under [@geometric-uncertaintaccuracy] and [@instrument]. | Sub-pixel accuracuncertainty is achieved relative to an identified absolute independent terrestrial referencing system (such as a national map grid). A consistent gridding/sampling frame is necessary to meet this requirement. Relevant metadata must be provided under [@geometric-uncertaintaccuracy] and [@instrument].
ST | Sub-pixel uncertaintaccuracy is achieved relative to an identified absolute independent terrestrial referencing system (such as a national map grid). A consistent gridding/sampling frame is necessary to meet this requirement. Relevant metadata must be provided under [@geometric-uncertainty] and [@instrument]. | Sub-pixel accuracuncertainty is achieved relative to an identified absolute independent terrestrial referencing system (such as a national map grid). A consistent gridding/sampling frame is necessary to meet this requirement. Relevant metadata must be provided under [@geometric-uncertaintaccuracy] and [@instrument].
Internal notes: ST 6.0 already aligned the metadata references ([@geometric-uncertainty]); remaining differences to the proposal: "accuracy" vs "uncertainty", "0.5 pixel" vs "0.5-pixel", and the gridding/sampling sentence. Will accept any proposal for consistency (action: Ferran and Peter). In the same approach as AR, ST decided to replace "Accuracy" with "Uncertainty" across the document.

## Slide 12
Geometric Correction (AR, NLSR, SR, ST) (cont.)
PFS | Current Goal Notes | Proposed Goal Notes
AR | This requirement is intended to enable interoperability between imagery from different platforms that meet this level of correction, and with non-image spatial data such as GIS layers and terrain models. (differs only in punctuation/whitespace) | The only question here is: with or without comma?
NLSR, SR (baseline) | This requirement is intended to enable interoperability between imagery from different platforms that meet this level of correction, and with non-image spatial data such as GIS layers and terrain models. | 
ST | This requirement is intended to enable interoperability between imagery from different platforms that meet this level of correction, and with non-image spatial data such as GIS layers and terrain models. | 
Notes: PROPOSAL:
**Threshold — description**:
```
Sub-pixel uncertainty is achieved in **relative** geolocation, that is, the pixels from the same instrument and platform are consistently located, and are thus comparable, through time. Sub-pixel uncertainty is taken to be less than or equal to 0.5-pixel radial root mean square error (rRMSE) or equivalent in Circular Error Probability (CEP) relative to a defined reference image. A consistent gridding/sampling frame is used, including common cell size, origin, and nominal sample point location within the cell (centre, ll, ur).
Relevant metadata must be provided under [@geometric-uncertainty] and [@instrument].
```
**Threshold — notes**:
```
1. The threshold level will not necessarily enable interoperability between data from different sources as the geometric corrections for each of the sources may differ.
2. It is useful to note if the sensor is used at its native resolution before geometric correction or that some resampling must be done.
```
**Goal — description**:
```
Sub-pixel uncertainty is achieved relative to an identified absolute independent terrestrial referencing system (such as a national map grid). Relevant metadata must be provided under Section “General Metadata: Geometric Uncertainty of the Data” and Section “General Metadata: Instrument”.
```
**Goal — notes (NLSR, SR, ST)**:
```
This requirement is intended to enable interoperability between imagery from different platforms that meet this level of correction and with non-image spatial data such as GIS layers and terrain models.
```
INTERNAL NOTES:
ST 6.0 already aligned the metadata references ([@geometric-uncertainty]); remaining differences to the proposal: "accuracy" vs "uncertainty", "0.5 pixel" vs "0.5-pixel", and the gridding/sampling sentence.
ST: requirement not yet touched; will accept any proposal for consistency (action: Ferran and Peter). In the same approach as AR, ST decided to replace "Accuracy" with "Uncertainty" across the document.

## Slide 13
Ozone Corrections (AR, SR)
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | Data is corrected for ozone if spectral bands are affected. | (keep as is)
SR | (not set) | (keep as is)
PFS | Current Threshold Notes | Proposed Threshold Notes
AR (baseline) | Relevant metadata must be provided in [@geometric-uncertainty] and [@instrument]. See @dekeukelaere2018, @harmel2018, @mobley2016, @pahlevan2017, @pahlevan2021, and @vanhellemont2019. | (keep as is)
SR | (no notes) | (keep as is)
PFS | Current Goal Description | Proposed Goal Description
AR | (not set) | (keep as is)
SR (baseline) | Data is corrected for ozone. Relevant metadata must be provided under [@geometric-accuracy] and [@instrument]. Metadata contains a single DOI landing page with references to: - a citable peer-reviewed algorithm - technical documentation regarding the implementation of that algorithm | Data is corrected for ozone if spectral bands are affected.
Internal notes: For DOI related discussions see "DOIs" slide.
Notes: PROPOSAL:
**Goal — description (SR)**:
```
Data is corrected for ozone if spectral bands are affected.
```
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.

## Slide 14
Water Vapour Corrections (AR, SR)
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | Corrections are applied for water vapour if spectral bands are affected. | (keep as is)
SR | Corrections are applied for water vapour if spectral bands are affected.. Metadata contains a single DOI landing page with references to: - a citable peer-reviewed algorithm - technical documentation regarding the implementation of that algorithm | Corrections are applied for water vapour. Metadata contains a single DOI landing page with references to: - a citable peer-reviewed algorithm - technical documentation regarding the implementation of that algorithm if spectral bands are affected.
PFS | Current Threshold Notes | Proposed Threshold Notes
AR | (no notes) | (keep as is)
SR (baseline) | Examples of technical documentation include an Algorithm Theoretical Basis Document, product user guide, etc. | DELETE NOTE
Internal notes: For DOI related discussions see "DOIs" slide.
Notes: PROPOSAL:
**Threshold — description (SR)**:
```
Corrections are applied for water vapour if spectral bands are affected.
```
**Threshold — notes (SR)**: Remove
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.

## Slide 15
Measurement Normalisation (AR, NLSR, SR)
PFS | Current Goal Description | Proposed Goal Description
AR (baseline) | Measurements are normalised (to nadir) to remove the effect of bidirectional dependence of the upwelling radiance on observation and solar-illumination geometries. | (keep as is)
NLSR | Measurements are normalised for viewing conditions (i.e., nadir view angle). This may include radiative transfer modelling. | Measurements are normalised (to nadir) to remove the effect of bidirectional dependence of the upwelling radiance on observation and solar-illumination geometries.
SR | Measurements are normalised for solar and viewing conditions (i.e., nadir view angle and average solar angles). This may include terrain illumination and/or Bi-Directional Reflectance Function (BRDF) correction. | Measurements are normalised (to nadir) to remove the effect of bidirectional dependence of the upwelling radiance on observation and solar-illumination geometries.
PFS | Current Goal Notes | Proposed Goal Notes
AR | (no notes) | (keep as is)
NLSR (baseline) | Information on measurement normalisation should be available in the metadata as a single DOI landing page. | DELETE NOTE
SR | Information on measurement normalisation should be available in the metadata as a single DOI landing page. | DELETE NOTE
Internal notes: For DOI related discussions see "DOIs" slide.
Notes: PROPOSAL:
**Goal — description (NLSR, SR)**:
```
Measurements are normalised (to nadir) to remove the effect of bidirectional dependence of the upwelling radiance on observation and solar-illumination geometries.
```
**Goal — notes (NLSR, SR)**: Remove
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.

## Slide 16
Measurement Uncertainty (AR, NLSR, SR, ST)
PFS | Current Description | Proposed Description
AR | (not set) | (keep as is)
NLSR, SR (baseline) | Note: In current practice, users determine fitness for purpose based on knowledge of the lineage of the data, rather than on a specific estimate of measurement uncertainty. | DELETE? (BUT: AR has a similar description, see below)
ST | (not set) | (keep as is)
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | An estimate of the uncertainty of the values is provided in measurement units, following the BIPM Guide to the Expression of Uncertainty in Measurement (GUM). | A self-assessed declaration of per-pixel measurement uncertainty, following Section 3.2.4 (Uncertainty Characterization) of the Joint Earth Observation Mission Quality Assessment Framework - Optical Guidelines is provided, meeting the Basic or Good criteria.
NLSR, SR | (not set) | A self-assessed declaration of per-pixel measurement uncertainty, following Section 3.2.4 (Uncertainty Characterization) of the Joint Earth Observation Mission Quality Assessment Framework - Optical Guidelines is provided, meeting the Basic or Good criteria.
ST | A self-assessed declaration of per-pixel measurement uncertainty, following Section 3.2.4 (Uncertainty Characterization) of the Joint Earth Observation Mission Quality Assessment Framework - Optical Guidelines is provided, meeting the Basic or Good criteria. | (keep as is)
PFS | Current Threshold Notes | Proposed Threshold Notes
AR (baseline) | In current practice, users determine fitness for purpose based on knowledge of the lineage of the data, rather than on a specific estimate of measurement uncertainty. See @gum_6_2020 and @vabson2024. | (keep as is)
NLSR, SR | (no notes) | (keep as is)
ST | (no notes) | (keep as is)

## Slide 17
Measurement Uncertainty (AR, NLSR, SR, ST) (cont.)
PFS | Current Goal Description | Proposed Goal Description
AR | (not set) | A self-assessed declaration of per-pixel measurement uncertainty, following Section 3.2.4 (Uncertainty Characterization) of the Joint Earth Observation Mission Quality Assessment Framework - Optical Guidelines is provided, meeting the Excellent or Ideal criteria.
NLSR, SR (baseline) | An estimate of the certainty of the values is provided in measurement units. | A self-assessed declaration of per-pixel measurement uncertainty, following Section 3.2.4 (Uncertainty Characterization) of the Joint Earth Observation Mission Quality Assessment Framework - Optical Guidelines is provided, meeting the Excellent or Ideal criteria.
ST | A self-assessed declaration of per-pixel measurement uncertainty, following Section 3.2.4 (Uncertainty Characterization) of the Joint Earth Observation Mission Quality Assessment Framework - Optical Guidelines is provided, meeting the Excellent or Ideal criteria. | (keep as is)
PFS | Current Goal Notes | Proposed Goal Notes
AR | (no notes) | (see ST)
NLSR, SR (baseline) | This is a requirement for SI traceability. See also [@traceability]. Information on measurement uncertainty should be available in the metadata as a single DOI landing page. | DELETE (see ST)
ST | https://science.nasa.gov/wp-content/uploads/2026/05/joint-optical-guidelines-jul2025-signed.pdf | Should this get come context instead of a plain link? Or be listed as reference? Should all other PFS also link to this document?
Internal notes: For DOI related discussions see "DOIs" slide.
ST updated this requirement following WGCV's recommendation to include uncertainty information at the threshold level, including the ESA-NASA-USGS quality guidelines, and proposes adopting it for all optical PFS; it also helps address the algorithms discussion (issue #84). This would constitute a major update for SR and NLSR and potentially a minor update for AR.

## Slide 18
Algorithms (AR, NLSR, SR, ST)
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | All algorithms and the sequence in which they were applied in the generation process are identified. Algorithms must be published and validated, and a description of the validation process is included. | (keep as is)
NLSR, SR | All algorithms, and the sequence in which they were applied in the generation process, are identified in the metadata. For example, these may be available through Algorithm Theoretical Basis documents. | All algorithms and the sequence in which they were applied in the generation process are identified in the metadata. For example, these may be available through Algorithm Theoretical Basis documents. Algorithms must be published and validated, and a description of the validation process is included.
ST | (not set) | (keep as is)
PFS | Current Threshold Notes | Proposed Threshold Notes
AR (baseline) | It is possible that corrections are applied through non-disclosed processes. CEOS-ARD does not require full and open data and methods. | (keep as is)
NLSR, SR | Information on algorithms should be available in the metadata as a single DOI landing page. | It is possible that corrections are applied through non-disclosed processes. CEOS-ARD does not require full and open data and methods.
ST | (no notes) | (keep as is)

## Slide 19
Algorithms (AR, NLSR, SR, ST) (cont.)
PFS | Current Goal Description | Proposed Goal Description
AR | (not set) | (keep as is)
NLSR, SR (baseline) | As threshold, but only algorithms that have been published in a peer-reviewed journal. | As threshold, but onlyll algorithms that have beenand the sequence in which they were applied in the generation process are identified. Algorithms must be published in a peer-reviewed journaland validated, and a description of the validation process is included.
ST | As threshold, but onlyll algorithms that have beenand versions, and the sequence in which they were applied in the generation process, are identified and published in a peer-reviewed journal. (optional) | All algorithms and versions, and the sequence in which they were applied in the generation process, are identified and. Algorithms must be published in a peer-reviewed journaland validated, and a description of the validation process is included.
PFS | Current Goal Notes | Proposed Goal Notes
AR | (no notes) | (keep as is)
NLSR, SR (baseline) | It is possible that high-quality corrections are applied through non-disclosed processes. CEOS-ARD does not per-se require full and open data and methods. Information on algorithms should be available in the metadata as a single DOI landing page. | DELETE
ST | (no notes) | (keep as is)
Internal notes: For DOI related discussions see "DOIs" slide.
ST agrees to adopt the AR requirement with swapped levels and without the note: with an uncertainty requirement at threshold, full provision of algorithm information is not required at threshold too, aiding commercial sector compliance (issue #55). Should we aim for a consistent requirement here? With the current proposal ST and AR/SR/NLSR would still differ.
Notes: PROPOSAL:
**Threshold — description (NLSR, SR, ST)**: Remove
**Threshold — notes (AR)**: Remove
**Goal — description (NLSR, SR, ST)**:
```
All algorithms and the sequence in which they were applied in the generation process are identified.
Algorithms must be published and validated, and a description of the validation process is included.
```
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.
ST agrees to adopt the AR requirement with swapped levels and without the note: with an uncertainty requirement at threshold, full provision of algorithm information is not required at threshold too, aiding commercial sector compliance (issue #55).

## Slide 20
Auxiliary Data (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL)
PFS | Current Threshold Description | Proposed Threshold Description
AR, ST (baseline) | Lists the sources of auxiliary data used in the generation process. | (keep as is)
NLSR, SR | ListThe metadata identifies the sources of auxiliary data used in the generation process., ideally expressed as a single DOI landing page. | The metadata identifieLists the sources of auxiliary data used in the generation process, ideally expressed as a single DOI landing page. .
CB, GSLC, INSAR, NRB, ORB, POL | (not set) | (keep as is)
PFS | Current Threshold Notes | Proposed Threshold Notes
AR, ST | (no notes) | Auxiliary data includes DEMs, and any additional data sources used in the generation of the product.
NLSR, SR (baseline) | Auxiliary data includes DEMs, aerosols, etc. data sources. | Auxiliary data includes DEMs, aerosols, etc. and any additional data sources used in the generation of the product.
CB, GSLC, INSAR, NRB, ORB, POL | (no notes) | (keep as is)

## Slide 21
Auxiliary Data (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL) (cont.)
PFS | Current Goal Description | Proposed Goal Description
AR, ST (baseline) | As threshold, but information on auxiliary data should be available for free online download, contemporaneously with the product or through a link to the source. | (keep as is)
NLSR, SR | As threshold, but information on auxiliary data should be available in the metadata as a single DOI landing page and is also available for free online download, contemporaneously with the product or through a link to the source. | As threshold, but information on auxiliary data should be available in the metadata as a single DOI landing page and is also available for free online download, contemporaneously with the product or through a link to the source.
CB, GSLC, INSAR, NRB, ORB, POL | The metadata identifies the sources of auxiliary data used in the generation process, ideally expressed as DOIs. | The metadata identifieLists the sources of auxiliary data used in the generation process, ideally expressed as DOIs.
PFS | Current Goal Notes | Proposed Goal Notes
AR, ST | (no notes) | (keep as is)
NLSR, SR | (no notes) | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL (baseline) | Auxiliary data includes DEMs, etc., and any additional data sources used in the generation of the product. | Auxiliary data includes DEMs, etc. and any additional data sources used in the generation of the product.
Internal notes: For DOI related discussions see "DOIs" slide.
We should consider fully aligning those requirements, only differing between whether they are goal or threshold.
Notes: PROPOSAL:
**Threshold — description (NLSR, SR)**:
```
Lists the sources of auxiliary data used in the generation process.
```
**Threshold — notes (NLSR, SR)**:
```
Auxiliary data includes DEMs, etc., and any additional data sources used in the generation of the product.
```
**Goal — description (NLSR, SR)**:
```
As threshold, but information on auxiliary data should be available for free online download, contemporaneously with the product or through a link to the source.
```
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.
The SAR variant only defines a goal; consider adding the aligned threshold requirement there as well.

## Slide 22
metadata/crs-* (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL)
PFS | Current Title | Proposed Title
AR (baseline) | Coordinate Reference System | (keep as is)
NLSR, SR, ST | Coordinate Reference System | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | Product Coordinate Reference System | Product Coordinate Reference System
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | The coordinate reference system that has been used is detailed. | (keep as is)
NLSR, SR, ST | The metadata lists the coordinate reference system that has been used is detailed. | The metadata lists the coordinate reference system that has been used is detailed.
CB, GSLC, INSAR, NRB, ORB, POL | The metadata lists the map projection (or geographical coordinates, if applicable) that was used and any relevant parameters required to geolocate data in that map projection, expressed in a standardised format (e.g., WKT). Indicate EPSG code, if defined for the CRS. | (keep as is)
Internal notes: The SAR variant additionally requires a standardised format (e.g., WKT) and the EPSG code — consider adopting this for the optical PFS as well? This would remove the Map Projection requirement in Optical.
Notes: PROPOSAL:
**Title (CB, GSLC, INSAR, NRB, ORB, POL)**:
```
Coordinate Reference System
```
**Threshold — description (NLSR, SR, ST)**:
```
The coordinate reference system that has been used is detailed.
```
INTERNAL NOTES:
The SAR variant additionally requires a standardised format (e.g., WKT) and the EPSG code — consider adopting this for the optical PFS in a future revision.

## Slide 23
Map Projection (AR, NLSR, SR, ST)
PFS | Current Threshold Description | Proposed Threshold Description
AR, ST (baseline) | The map projection that has been used and any relevant parameters required in relation to use of data in that map projection is detailed. | (keep as is)
NLSR | The metadata lists the map projection that has been used and any relevant parameters required in relation to use of data in that map projection is detailed. | The metadata lists the map projection that has been used and any relevant parameters required in relation to use of data in that map projection is detailed.
SR | The metadata lists the map projection that has been used (or geographical coordinates, if applicable) and any relevant parameters required in relation to use of data in that map projection is detailed. | The metadata lists the map projection that has been used (or geographical coordinates, if applicable) and any relevant parameters required in relation to use of data in that map projection is detailed.
Internal notes: Remove requirement and merge it with the CRS requirement?
Notes: PROPOSAL:
**Threshold — description (NLSR, SR)**:
```
The map projection that has been used and any relevant parameters required in relation to use of data in that map projection is detailed.
```
INTERNAL NOTES:
Resolved: ST now uses the AR requirement directly (map-projection-st was removed). ST: it is unclear why the threshold became "Not Required" (introduced somewhere between v3.0 and v4.0); the ST team intends to adopt the AR PFS approach.

## Slide 24
metadata/data-access-* (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL)
PFS | Current Title | Proposed Title
AR, NLSR, SR, ST (baseline) | Data Access | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | Product Data Access | Product Data Access
CB, GSLC, INSAR, NRB, ORB, POL | Source Data Access | Source Data Access
PFS | Current Threshold Description | Proposed Threshold Description
AR, NLSR, SR, ST (baseline) | Information on data access should be available in the metadata as a single DOI landing page. | The location from where the data can be retrieved is identified, expressed as a URL or DOI.
CB, GSLC, INSAR, NRB, ORB, POL | Processing parameters details of the CEOS-ARD product: - Processing facility - Processing date - Software version - Location from where CEOS-ARD product can be retrieved, expressed as a URL or DOI. | Split into separate requirements. Oine for data access, one for the processing details. The location from where the data can be retrieved is identified, expressed as a URL or DOI. and Processing parameters details of the CEOS-ARD product: - Processing facility - Processing date - Software version
CB, GSLC, INSAR, NRB, ORB, POL | The metadata identifies the location from where the source data can be retrieved, expressed as a URL or DOI. | The location from where the data can be retrieved is identified, expressed as a URL or DOI.

## Slide 25
metadata/data-access-* (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL) (cont.)
PFS | Current Threshold Notes | Proposed Threshold Notes
AR, NLSR, SR, ST (baseline) | Manual and offline interaction action (e.g., login) may be required. | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | (no notes) | Manual and offline interaction action (e.g., login) may be required.
CB, GSLC, INSAR, NRB, ORB, POL | (no notes) | Manual and offline interaction action (e.g., login) may be required.
PFS | Current Goal Description | Proposed Goal Description
AR, NLSR, SR, ST | (not set) | An online location is identified from where the data can be consistently and reliably retrieved by a computer algorithm without any manual intervention being required.
CB, GSLC, INSAR, NRB, ORB, POL (baseline) | The metadata identifies an online location from where the data can be consistently and reliably retrieved by a computer algorithm without any manual intervention being required. | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | The metadata identifies an online location from where the data can be consistently and reliably retrieved by a computer algorithm without any manual intervention being required. | (keep as is)
Internal notes: For DOI related discussions see "DOIs" slide.
The current optical threshold only contains the DOI landing page sentence, which moves to category level — the proposal gives Data Access a concrete requirement, aligned with the SAR product variant. The split into Product/Source Data Access remains specific to the SAR family.

## Slide 26
metadata/geo-area-* (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL)
PFS | Current Title | Proposed Title
AR, NLSR, SR, ST (baseline) | Geographical Area | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | Product Geographical AreaExtent | Product Geographical ExtentArea
PFS | Current Threshold Description | Proposed Threshold Description
AR, NLSR, SR, ST (baseline) | The surface location to which the data relates is identified, typically as a series of four corner points, expressed in an accepted coordinate reference system (e.g., WGS84). | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | The geometry of the SAR image footprint expressed in longitude/latitude based on WGS84 (EPSG 4326), in a standardised format (e.g., WKT Polygon). | (keep as is)
PFS | Current Goal Description | Proposed Goal Description
AR, NLSR, SR, ST (baseline) | The geographic area covered by the observations is identified specifically, such as through a set of coordinates of a closely bounding polygon. The location to which each pixel refers is identified (or can be reliably determined) with the projection system (if any) and reference datum provided. | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | (not set) | (keep as is)
Internal notes: SAR has extent and area separately, Optical has extent as goal and area as goal. Can we unify this?

## Slide 27
Geometric Correction Methods (AR, NLSR, SR, ST)
PFS | Current Goal Description | Proposed Goal Description
AR, ST (baseline) | Information on geometric correction source and methods are provided, including reference database and auxiliary data such as elevation model(s) and reference chip-sets. | (keep as is)
NLSR, SR | Information on geometric correction source and methods are providedmethods should be available in the metadata as a single DOI landing page, including reference database and auxiliary data such as elevation model(s) and reference chip-sets. | Information on geometric correction methods should be available in the metadata as a single DOI landing pagesource and methods are provided, including reference database and auxiliary data such as elevation model(s) and reference chip-sets.
Internal notes: For DOI related discussions see "DOIs" slide.
Notes: PROPOSAL:
**Goal — description (NLSR, SR)**:
```
Information on geometric correction source and methods are provided, including reference database and auxiliary data such as elevation model(s) and reference chip-sets.
```
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.
Resolved for ST: it now uses the AR requirement directly (geometric-correction-methods-st was removed). ST team: agree to adopt the AR approach.

## Slide 28
Instrument (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL)
PFS | Current Threshold Description | Proposed Threshold Description
AR, ST (baseline) | The instrument used to collect the data is identified. | The instrument used to collect the data is identified.: - Satellite name - Instrument name
NLSR, SR | The instrument used to collect the data is identified in the metadata. | The instrument used to collect the data is identified in the metadata.: - Satellite name - Instrument name
CB, GSLC, INSAR, NRB, ORB, POL | The instrument used to collect the data is identified. in the metadata: - Satellite name - Instrument name | The instrument used to collect the data is identified in the metadata: - Satellite name - Instrument name
PFS | Current Goal Description | Proposed Goal Description
AR, ST (baseline) | As threshold, with references to the relevant “CEOS Missions, Instruments, and Measurements Database” record ([database.eohandbook.com](https://database.eohandbook.com)). | As threshold, with references to the relevant “CEOS Missions, Instruments, and Measurements Database” record ([database.eohandbook.com](https://database.eohandbook.com)(MIM) database record (https://ceos.org/mim-database).
NLSR, SR | As threshold, but information should be available in the metadata as a single DOI landing page with references to the relevant “CEOS Missions, Instruments, and Measurements Database” record ([database.eohandbook.com](https://database.eohandbook.com)). record. | As threshold, but information should be available in the metadata as a single DOI landing page with references to the relevant CEOS Missions, Instruments, and Measurements D(MIM) database record. (https://ceos.org/mim-database).
CB, GSLC, INSAR, NRB, ORB, POL | As threshold, but using [CEOS Mission-Instruments-Measurements (MIM) database](https://ceos.org/mim-database) as reference. | As threshold, but using [with references to the relevant CEOS Mission-s, Instruments-, and Measurements (MIM) database] record (https://ceos.org/mim-database) as reference.
Internal notes: For DOI related discussions see "DOIs" slide.
The MIM database URL (ceos.org/mim-database) supersedes the old database.eohandbook.com link used by AR. Should we rename the title due to listing also the satellite?
Notes: PROPOSAL:
**Threshold — description**:
```
The instrument used to collect the data is identified:
- Satellite name
- Instrument name
```
**Goal — description**:
```
As threshold, with references to the relevant CEOS Missions, Instruments, and Measurements (MIM) database record (https://ceos.org/mim-database).
```
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.
The MIM database URL (ceos.org/mim-database) supersedes the old database.eohandbook.com link used by AR.

## Slide 29
Metadata Machine Readability (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL)
PFS | Current Threshold Description | Proposed Threshold Description
AR, NLSR, SR, ST (baseline) | Metadata is provided in a structure that enables a computer algorithm to be used to consistently and automatically identify and extract each component part for further use. | Metadata is provided in a structure that enables a computer algorithm to be used to consistently and automatically identify and extract each component part/variable for further use.
CB, GSLC, INSAR, NRB, ORB, POL | Metadata is provided in a structure that enables a computer algorithm to be used to consistently and automatically identify and extract each component part/variable for further use. | (keep as is)
AR, NLSR, SR | Metadata is provided in a structure that enables a computer algorithm to be used to consistently and automatically identify and extract each component part for further use. | Metadata is provided in a structure that enables a computer algorithm to be used to consistently and automatically identify and extract each component part/variable for further use.
PFS | Current Goal Description | Proposed Goal Description
AR, NLSR, SR, ST (baseline) | As threshold, but metadata should be provided in a community endorsed standard that facilitates machine-readability, such as ISO 19115-2. | As threshold, but metadata should beis provided in a community endorsed standard that facilitates machine-readability, such as CEOS-ARD Metadata Specifications, ISO 19115-2, STAC, the Climate and Forecast (CF) convention, or the Attribute Convention for Data Discovery (ACDD).
CB, GSLC, INSAR, NRB, ORB, POL | As threshold, but metadata should be providedis formatted in accordance with the latest corresponding CEOS-ARD SAR Metadata Specifications, or in a community endorsed standard that facilitates machine-readability, such as ISO 19115-2, Climate and Forecast (CF) convention and the Attribute Convention for Data Discovery (ACDD), etc. | As threshold, but metadata is formatted in accordance with the latest corresponding CEOS-ARD SAR Metadata Specifications, orprovided in a community endorsed standard that facilitates machine-readability, such as CEOS-ARD Metadata Specifications, ISO 19115-2, STAC, the Climate and Forecast (CF) convention and, or the Attribute Convention for Data Discovery (ACDD), etc.
AR, NLSR, SR | (not set) | As threshold, but metadata is provided in a community endorsed standard that facilitates machine-readability, such as CEOS-ARD Metadata Specifications, ISO 19115-2, STAC, the Climate and Forecast (CF) convention, or the Attribute Convention for Data Discovery (ACDD).
Internal notes: Provide this only in the General Metadata, and not provide this in Per-Pixel Metadata?
Notes: PROPOSAL:
**Threshold — description (AR, NLSR, SR, ST)**:
```
Metadata is provided in a structure that enables a computer algorithm to be used to consistently and automatically identify and extract each component/variable for further use.
```
**Goal — description (AR, NLSR, SR, ST)**:
```
As threshold, but metadata should be provided in a community endorsed standard that facilitates machine-readability, such as ISO 19115-2, the Climate and Forecast (CF) convention, or the Attribute Convention for Data Discovery (ACDD).
```
INTERNAL NOTES:
The reference to the CEOS-ARD SAR Metadata Specifications remains specific to the SAR variant. The per-pixel variant has no goal — consider adding the same goal (optional) there for consistency.

## Slide 30
Processing Chain Provenance (AR, NLSR, SR, ST)
PFS | Current Threshold Description | Proposed Threshold Description
AR | (not set) | (keep as is)
NLSR | (not set) | (keep as is)
SR | (not set) | (keep as is)
ST (baseline) | The provider attaches to each delivered dataset (delivery unit) a code which allows them to reconstruct the exact processing environment (software versions, calibration files, parameter settings) in which this particular output was produced. | (keep as is)
PFS | Current Goal Description | Proposed Goal Description
AR (baseline) | Information on processing chain provenance should be available with a detailed description of the processing steps used to generate the product, including the versions of software used, giving full transparency to the users. | (keep as is)
NLSR | Information on processing chain provenance should be available with ain the metadata as a single DOI landing page containing detailed description of the processing steps used to generate the product, includingthe organization that performed the processing, and the versions of software used, giving full transparency to the users. | Information on processing chain provenance should be available in the metadata as a single DOI landing page containingwith a detailed description of the processing steps used to generate the product, the organization that performed the processing, andincluding the versions of software used, giving full transparency to the users.
SR | Information on processing chain provenance should be available with ain the metadata as a single DOI landing page containing detailed description of the processing steps used to generate the product, including the versions of software used, giving full transparency to the users. | Information on processing chain provenance should be available in the metadata as a single DOI landing page containingwith a detailed description of the processing steps used to generate the product, including the versions of software used, giving full transparency to the users.
ST | As threshold, but the provider is also in grade to reproduce the exact same output. | (keep as is)
Internal notes: For DOI related discussions see "DOIs" slide.
ST 6.0 upgraded provenance to a threshold requirement (reconstructable processing environment) with a reproducibility goal (issue #58). Still under discussion in the ST team; current thinking remains to introduce the threshold requirement — consider adopting this approach for the other optical PFS. In the long-term, all PFS should probably follow the ST approach.

## Slide 31
Radiometric Accuracy (NLSR, SR, CB, GSLC, INSAR, NRB, ORB, POL)
PFS | Current Goal Description | Proposed Goal Description
CB, GSLC, INSAR, NRB, ORB, POL (baseline) | Uncertainty (e.g., bounds on $\gamma^0$ or $\sigma^0$) information is provided as document referenced as URL or DOI. SI traceability is achieved. | (keep as is)
NLSR, SR | The metadata includes metrics describing the assessed absolute radiometric uncertainty of the version of the data or product, expressed as absolute radiometric uncertainty relative to appropriate, known reference sites and standards (for example, pseudo-invariant calibration sites, rigorously collected field spectra, Rayleigh, DCC, etc.) | (keep as is)
PFS | Current Goal Notes | Proposed Goal Notes
CB, GSLC, INSAR, NRB, ORB, POL | (no notes) | (keep as is)
NLSR, SR (baseline) | Information on radiometric accuracy should be available in the metadata as a single DOI landing page. | DELETE NOTE
Internal notes: For DOI related discussions see "DOIs" slide.
ST dropped its radiometric accuracy requirement in ST 6.0 (the file was removed).
Remarks from the building blocks: NLSR/SR: What does DCC stand for? Add to glossary.
Notes: PROPOSAL:
**Goal — notes (NLSR, SR)**: Remove
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.
ST dropped its radiometric accuracy requirement in ST 6.0 (the file was removed).

## Slide 32
Sensor Calibration (AR, NLSR, SR, ST, GSLC, INSAR, NRB, ORB, POL)
PFS | Current Threshold Description | Proposed Threshold Description
AR, ST (baseline) | Binary description of calibrated/not calibrated only. | (keep as is)
NLSR, SR | (not set) | (keep as is)
GSLC, INSAR, NRB, ORB, POL | (not set) | (keep as is)
PFS | Current Goal Description | Proposed Goal Description
AR, ST (baseline) | Specification of sensor calibration parameters including history of onboard calibrations where available. | Sensor calibration parameters are identified or can be accessed using details included in the metadata. Ideally this would support machine-to-machine access.
NLSR, SR | Sensor calibration parameters are identified in the metadata or can be accessed using details included in the metadata. Ideally this would support machine-to-machine access. | Sensor calibration parameters are identified in the metadata or can be accessed using details included in the metadata. Ideally this would support machine-to-machine access.
GSLC, INSAR, NRB, ORB, POL | Sensor calibration parameters are identified in the metadata or can be accessed using details included in the metadata. Ideally this would support machine-to-machine access. | Sensor calibration parameters are identified in the metadata or can be accessed using details included in the metadata. Ideally this would support machine-to-machine access.
Internal notes: AR only has this required "Binary description of calibrated/not calibrated only." All SAR, SR, ST and NLSR = "Not required". Might already be captured in Github but should discuss if AR requirement should be adopted by SAR and other Optical PFSs.
PFS | Current Goal Notes | Proposed Goal Notes
AR, ST | (no notes) | (keep as is)
NLSR, SR (baseline) | Information on sensory calibration should be available in the metadata as a single DOI landing page. | DELETE NOTE
GSLC, INSAR, NRB, ORB, POL | (no notes) | (keep as is)

## Slide 33
Spectral Bands (AR, NLSR, SR, ST)
PFS | Current Threshold Description | Proposed Threshold Description
AR, ST (baseline) | Full spectral response function is provided. | Full sSpectral response function and method of assessment is provided.
NLSR, SR | The central wavelength for each band for which data is included is identified in the metadata, expressed in SI units. | Spectral response function and method of assessment is provided.
PFS | Current Goal Description | Proposed Goal Description
AR, ST | (not set) | (keep as is)
NLSR, SR (baseline) | As threshold, with instrument spectral response details (e.g., full spectral response function) also included or directly accessible using details in the metadata. Central wavelength and bandwidth at full-width half maximum value of the relative spectral response function are provided at least. | DELETE
PFS | Current Goal Notes | Proposed Goal Notes
AR, ST | (no notes) | (keep as is)
NLSR, SR (baseline) | Information on spectral bands should be available in the metadata as a single DOI landing page. | DELETE
Internal notes: For DOI related discussions see "DOIs" slide. Scientifically the spectral response function is important, but common metadata usually lists bands with central wavelength / FWHM / etc. Should we aim for this as well?
Notes: PROPOSAL:
**Threshold — description**:
```
Spectral response function and method of assessment is provided.
```
**Goal — description (NLSR, SR)**: Remove
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.
ST has proposed to adopt the AR PFS requirement.

## Slide 34
metadata/time-* (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL)
PFS | Current Title | Proposed Title
AR, ST (baseline) | Data Collection Time | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | Data Collection Time | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | Source Data Acquisition Time | Source Data AcquisiData Collection Time
NLSR, SR | Data Collection Time | (keep as is)
Internal notes:
SAR uses times in general metadata and source metadata, but requesting pretty much the same. This could be a generic building block. time-sar.yaml has a ISO 8601 goal requirement, but time-source.yaml does not. Should it?

## Slide 35
metadata/time-* (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL)
PFS | Current Threshold Description | Proposed Threshold Description
AR, ST (baseline) | The beginning and end of the data collection time is expressed in date/time and identified in the metadata consistent with ISO 8601. The time is expressed with the time offset from UTC unambiguously identified. | The beginning and end of the data collection time is expressed in date/time and identified in the metadata consistent with ISO 8601. The time is expressed with the time offset from UTC unambiguously identified. In the case of composite or mosaic products, the dates/times of the first and last data takes is provided with the product.
CB, GSLC, INSAR, NRB, ORB, POL | Number of source data acquisitions of the data collection is identified. The start and stop UTC time of data collection is identified in the metadata, expressed in date/time. In the case of composite or mosaic products, the dates/times of the first and last data takes is provided with the product. | Split into two separate requirements: Number of source data acquisitionsThe beginning and end of the data collection is identified. The start and stop UTC time of data collection istime is expressed in date/time and identified in the metadata, consistent with ISO 8601. The time is expressed in date/time.with the time offset from UTC unambiguously identified. In the case of composite or mosaic products, the dates/times of the first and last data takes is provided with the product. and Number of source data acquisitions of the data collection is identified.
CB, GSLC, INSAR, NRB, ORB, POL | The start date and time of source data is identified in the metadata, expressed in UTC in date and time, at least to the second. | The start date and time of source data isbeginning and end of the data collection time is expressed in date/time and identified in the metadata, consistent with ISO 8601. The time is expressed in UTC in date and time, at least to the secondwith the time offset from UTC unambiguously identified. In the case of composite or mosaic products, the dates/times of the first and last data takes is provided with the product.
NLSR, SR | The beginning and end of the data collection time is expressed in date/time and identified in the metadata consistent with ISO 8601. The time is, expressed in date/time, to the second, with the time offset from UTC unambiguously identified. | The beginning and end of the data collection time is expressed in date/time and identified in the metadata, consistent with ISO 8601. The time is expressed in date/time, to the second, with the time offset from UTC unambiguously identified. In the case of composite or mosaic products, the dates/times of the first and last data takes is provided with the product.

## Slide 36
metadata/time-* (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL) (cont.)
PFS | Current Goal Description | Proposed Goal Description
AR, ST (baseline) | As threshold, but information required to determine, within a stated uncertainty, when the individual observations were taken is available. | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | As threshold, but using ISO 8601 time format. | As threshold, but using ISO 8601 time formatinformation required to determine, within a stated uncertainty, when the individual observations were taken is available.
CB, GSLC, INSAR, NRB, ORB, POL | (not set) | As threshold, but information required to determine, within a stated uncertainty, when the individual observations were taken is available.
NLSR, SR | Acquisition time for each pixel is identified (or can be reliably determined) in the metadata, expressed in date/time at UTC, to the second. | As threshold, but information required to determine, within a stated uncertainty, when the individual observations were taken is available. and separate goal per-pixel requirement (for all Optical PFS?): Acquisition time for each pixel is identified (or can be reliably determined) in the metadata, expressed in date/time at UTC, to the second.

## Slide 37
metadata/traceability-* (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL)
PFS | Current Title | Proposed Title
AR (baseline) | Traceability | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | Traceability | (keep as is)
NLSR, SR | Traceability | (keep as is)
ST | Metrological Traceability of the Measurand to SI | Metrological Traceability of the Measurand to SI
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | Aquatic Reflectance (dimensionless) or the Remote Sensing Reflectance ($sr^{-1}$) of the water bodies ($AR = \pi \cdot R_{rs}$) is given. | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | (not set) | (keep as is)
NLSR, SR | (not set) | (keep as is)
ST | (not set) | (keep as is)
Internal notes:
Traceability was renamed to 'Metrological Traceability of the Measurand to SI' following the April Oversight Group meeting decision #6. We need to discuss whether this requirement need to be domain-specific or can be generic.

## Slide 38
metadata/traceability-* (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL) (cont.)
PFS | Current Goal Description | Proposed Goal Description
AR (baseline) | Data must be traceable to SI reference standard. | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL | Data must be traceable to SI reference standard. | (keep as is)
NLSR, SR | Data must be traceable to SI reference standard. | (keep as is)
ST | Data must be traceable to SI reference standard. Information on traceability should be available in the metadata as a single DOI landing page. | Data must be traceable to SI reference standard. Information on traceability should be available in the metadata as a single DOI landing page.
Internal notes:
Should all PFS follow ST or the other way around? See also DOI slides…

## Slide 39
metadata/traceability-* (AR, NLSR, SR, ST, CB, GSLC, INSAR, NRB, ORB, POL) (cont.)
PFS | Current Goal Notes | Proposed Goal Notes
AR | Relationship to [@relationshipuncertainty]. Traceability requires an estimate of measurement uncertainty. Information on traceability should be available in the metadata as a single DOI landing page. | (keep as is)
CB, GSLC, INSAR, NRB, ORB, POL (baseline) | Relationship to [@relationship]. Traceability requires an estimate of measurement uncertainty. Information on traceability should be available in the metadata as a single DOI landing page. | DELETE NOTE
NLSR, SR | Relationship to [@relationship]. Traceability requires an estimate of measurement uncertainty. Information on traceability should be available in the metadata as a single DOI landing page. | DELETE NOTE
ST | Relationship to [@relationship].SI Traceability requires an estimate of measurement uncertainty. Information on traceability should be available in the metadata as a single DOI landing page (see [@uncertainty]). | (keep as is)
Internal notes: For DOI related discussions see "DOIs" slide.
Notes: PROPOSAL:
**Title (ST)**:
```
Traceability
```
**Goal — description (ST)**:
```
Data must be traceable to SI reference standard.
```
**Goal — notes (CB, GSLC, INSAR, NRB, ORB, POL, NLSR, SR)**: Remove the DOI landing page note
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.

## Slide 40
Cloud (AR, NLSR, SR, ST)
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | Specification of whether a pixel is cloud or cloud-affected. | Specification of whether a pixel is cloud or cloud-affected.
ST | Specification of whether a pixel is cloud or cloud-affected. | (keep as is)
NLSR, SR | Metadata indicates whether a pixel is assessed as being cloud. | Specification of whether a pixel is cloud-affected.
PFS | Current Goal Description | Proposed Goal Description
AR (baseline) | As threshold, but clouds and cirrus clouds are differentiated. | As threshold, but information on cloud type or confidence is included.
ST | As threshold, but information on cloud type or confidence is included. | (keep as is)
NLSR, SR | As threshold, but information on cloud detection should be available in the metadata as a single DOI landing page. | As threshold, but information on cloud detection should be available in the metadata as a single DOI landing pagetype or confidence is included.
PFS | Current Goal Notes | Proposed Goal Notes
AR (baseline) | See @foga2017, @skakun2022, @zhu2012, and @zhu2015. | (keep as is)
ST | (no notes) | (keep as is)
NLSR, SR | (no notes) | (keep as is)
Internal notes: For DOI related discussions see "DOIs" slide.
Agreed to adopt the requirement with this simplified wording (matches the ST 6.0 texts; GitHub issue #112).
Notes: PROPOSAL:
**Threshold — description (AR, NLSR, SR)**:
```
Specification of whether a pixel is cloud-affected.
```
**Goal — description (AR, NLSR, SR)**:
```
As threshold, but information on cloud type or confidence is included.
```
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.
Agreed to adopt the requirement with this simplified wording (matches the ST 6.0 texts; GitHub issue #112).

## Slide 41
Cloud Shadow (AR, NLSR, SR, ST)
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | Specification of whether a pixel is cloud shadow or cloud shadow-affected. | Specification of whether a pixel is cloud shadow or cloud shadow-affected.
NLSR | (not set) | (keep as is)
ST | (not set) | (keep as is)
SR | Metadata indicates whether a pixel is assessed as being cloud shadow. | Metadata indicatesSpecification of whether a pixel is assessed as being cloud shadow-affected.
PFS | Current Goal Description | Proposed Goal Description
AR | (not set) | (keep as is)
NLSR (baseline) | Metadata indicates whether a pixel is assessed as being cloud shadow. Information on cloud shadow detection should be available in the metadata as a single DOI landing page. | Metadata indicatesSpecification of whether a pixel is assessed as being cloud shadow. Information on cloud shadow detection should be available in the metadata as a single DOI landing page-affected.
ST | Metadata indicatesSpecification of whether a pixel is assessed as being cloud shadow. Information on cloud shadow detection should be available in the metadata as a single DOI landing page-affected. | (keep as is)
SR | Metadata indicates whether a pixel is assessed as being cloud shadow. IAs threshold, but information on cloud shadow detection should be available in the metadata as a single DOI landing page. | (keep as is)
Internal notes: For DOI related discussions see "DOIs" slide. Should we have the „Information on cloud shadow detection should be available in the metadata [as a single DOI landing page.]“?
ST keeps it as a goal-only requirement (limited suitability for non-reflectance methods) — likely a requirement that stays unique for the ST PFS.

## Slide 42
per-pixel/incomplete-testing-* (AR, NLSR, SR, ST)
PFS | Current Title | Proposed Title
AR | Per-pixel Assessment | (keep as is)
ST (baseline) | Incomplete Testing | Per-pixel Assessment
NLSR, SR | Incomplete Testing | Per-pixel Assessment
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | Identifies pixels for which the per-pixel tests (below) have not all been successfully completed. | (keep as is)
ST | Identifies pixels for which the per-pixel tests (below2.3, 2.4, 2.6) have not all been successfully completed. | Replace the hard-coded test numbers with cross-references to the respective requirements
NLSR, SR | IThe metadata identifies pixels for which the per-pixel tests (below) have not all been successfully completed. | The metadata iIdentifies pixels for which the per-pixel tests (below) have not all been successfully completed.
PFS | Current Goal Description | Proposed Goal Description
AR (baseline) | Identifies which tests have and have not been successfully completed for each pixel. | (keep as is)
ST | Identifies which tests (2.3, 2.4, 2.5, 2.6, 2.8) have and have not been successfully completed for each pixel. | Replace the hard-coded test numbers with cross-references to the respective requirements
NLSR, SR | IThe metadata identifies which tests have, and have not, been successfully completed for each pixel. | The metadata iIdentifies which tests have, and have not, been successfully completed for each pixel.
Internal notes: ST added the explicit per-pixel test numbers deliberately (specifying them aids metadata machine readability and automated assessment), recognising that this diverges from the other PFS.
The hard-coded test numbers (2.3, 2.4, …) in the descriptions do not work in the building blocks — the requirement numbering is generated per PFS — and need to be changed (e.g. to cross-references). We either need to override this list per PFS or not provide a list.

## Slide 43
per-pixel/land-water-* (AR, NLSR, SR)
PFS | Current Title | Proposed Title
AR | Land/Water Mask | (keep as is)
NLSR (baseline) | Land/Water Mask | (keep as is)
SR | Land/Water Mask | (keep as is)
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | Specification of whether a pixel is less than 100% water covered due to land. | (keep as is)
NLSR | Metadata indicates whether a pixel is land or water. | Metadata indicatesSpecification of whether a pixel is land or water.
SR | (not set) | (keep as is)
PFS | Current Threshold Notes | Proposed Threshold Notes
AR (baseline) | See @jones2019, @mikelsons2021, and @pekel2016. | (keep as is)
NLSR | (no notes) | (keep as is)
SR | (no notes) | (keep as is)

## Slide 44
per-pixel/land-water-* (AR, NLSR, SR) (cont.)
PFS | Current Goal Description | Proposed Goal Description
AR | (not set) | (keep as is)
NLSR (baseline) | As threshold, information on land/water mask should be available in the metadata as a single DOI landing page. | As threshold, information on land/water mask should be available in the metadata as a single DOI landing page.
SR | As threshold, iThe metadata indicates whether a pixel is assessed as being land or water. Information on land/water mask should be available in the metadata as a single DOI landing page. | The metadata indicatesSpecification of whether a pixel is assessed as being land or water. Information on land/water mask should be available in the metadata as a single DOI landing page.
Internal notes: For DOI related discussions see "DOIs" slide.
ST replaced its Snow/Ice requirement with a combined "Surface" requirement (threshold: land or water, including the information source and other relevant surface characteristic classification; goal: as threshold, plus snow or ice; external data sources listed under Auxiliary Data) — could be considered for the other optical PFS. AR is still different, can we align?
Notes: PROPOSAL:
**Threshold — description (NLSR)**:
```
Specification of whether a pixel is land or water
```
**Goal — description (NLSR)**:
```
As threshold
```
**Goal — description (SR)**:
```
Specification of whether a pixel is land or water
```
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.
ST replaced its Snow/Ice requirement with a combined "Surface" requirement (threshold: land or water, including the information source and other relevant surface characteristic classification; goal: as threshold, plus snow or ice; external data sources listed under Auxiliary Data) — could be considered for the other optical PFS.

## Slide 45
No Data (AR, NLSR, SR, ST)
PFS | Current Threshold Description | Proposed Threshold Description
AR (baseline) | Pixels that do not correspond to an observation (e.g., empty pixels / invalid observations / below noise floor) are masked. | Pixels that do not correspond to an observation (‘No Data / Invalid / Falsified / Valid / Modelled’) are flagged.
ST | Pixels that do not correspond to an observation (‘No Data / Invalid / Falsified / Valid / Modelled’) are flagged. | (keep as is)
NLSR, SR | Pixels that do not correspond to an observation (e.g., ‘empty pixels / invalid observations / below noise floor) are mask’) are flagged. | Pixels that do not correspond to an observation (‘empty pixelsNo Data / Invalid / Falsified / Valid / Modelled’) are flagged.
Internal notes: ST proposes all other optical PFS adopt the five-class flag wording, addressing Peter's comment in issue #4.
Notes: PROPOSAL:
**Threshold — description (AR, NLSR, SR)**:
```
Pixels that do not correspond to an observation (‘No Data / Invalid / Falsified / Valid / Modelled’) are flagged.
```
**Goal — description (AR, NLSR, SR, ST)**:
```
As threshold.
```
INTERNAL NOTES:
ST proposes all other optical PFS adopt the five-class flag wording, addressing Peter's comment in issue #4.

## Slide 46
Saturation (AR, NLSR, SR, ST)
PFS | Current Threshold Description | Proposed Threshold Description
AR, ST (baseline) | Specification of whether there is pixel radiometric saturation at Level 1 in one or more spectral bands. | (keep as is)
NLSR, SR | Metadata indicates where one or more pixel in the input spectral bands are saturated. | Specification of whether there is pixel radiometric saturation at Level 1 in one or more spectral bands.
PFS | Current Goal Description | Proposed Goal Description
AR, ST (baseline) | As threshold, with specification of which pixels are radiometrically saturated for each spectral band. | (keep as is)
NLSR, SR | As threshold, with specification ofMetadata indicates which pixels are radiometrically saturated for each spectral band. | Metadata indicatesAs threshold, with specification of which pixels are radiometrically saturated for each spectral band.
Notes: PROPOSAL:
**Threshold — description (NLSR, SR)**:
```
Specification of whether there is pixel radiometric saturation at Level 1 in one or more spectral bands.
```
**Goal — description (NLSR, SR)**:
```
As threshold, with specification of which pixels are radiometrically saturated for each spectral band.
```

## Slide 47
Snow/Ice Mask (NLSR, SR)
PFS | Current Threshold Description | Proposed Threshold Description
NLSR (baseline) | Metadata indicates whether a pixel is snow/ice. | Metadata indicatesSpecification of whether a pixel is snow/ice.
SR | (not set) | (keep as is)
PFS | Current Goal Description | Proposed Goal Description
NLSR (baseline) | As threshold, information on snow/ice mask should be available in the metadata as a single DOI landing page. | As threshold, information on snow/ice mask should be available in the metadata as a single DOI landing page.
SR | As threshold, iThe metadata indicates whether a pixel is assessed as being snow/ice or not. Information on snow/ice mask should be available in the metadata as a single DOI landing page. | Specification of whether a pixel is snow/ice
Internal notes: For DOI related discussions see "DOIs" slide.
ST replaced its Snow/Ice requirement with a combined "Surface" requirement (threshold: land or water, including the information source and other relevant surface characteristic classification; goal: as threshold, plus snow or ice) — could be considered for the other optical PFS.
Notes: PROPOSAL:
**Threshold — description (NLSR)**:
```
Specification of whether a pixel is snow/ice
```
**Goal — description (NLSR)**:
```
As threshold
```
**Goal — description (SR)**:
```
Specification of whether a pixel is snow/ice
```
INTERNAL NOTES:
For DOI related discussions see "DOIs" slide.
ST replaced its Snow/Ice requirement with a combined "Surface" requirement (threshold: land or water, including the information source and other relevant surface characteristic classification; goal: as threshold, plus snow or ice) — could be considered for the other optical PFS.

## Slide 48
Terrain Occlusion (NLSR, SR, ST)
PFS | Current Goal Description | Proposed Goal Description
ST (baseline) | Identifies pixels that are not visible to the sensor due to terrain occlusion during off-nadir viewing. | IdentifiesSpecification of whether pixels that are not visible to the sensor due to terrain occlusion during off-nadir viewing.
NLSR, SR | IdentifiThe metadata indicates pixels that are not visible to the sensor due to terrain occlusion during off-nadir viewing. | The metadata indicatesSpecification of whether pixels that are not visible to the sensor due to terrain occlusion during off-nadir viewing.
Internal notes: ST removed the threshold ("Not required.") — the requirement is now goal-only like the SR/NLSR variant.
Terrain Occlusion was introduced to the ST PFS with the initial pull request (hence visible in the draft but not in the released version). ST proposes to adopt the consistent wording proposed here.
Notes: PROPOSAL:
**Goal — description (NLSR, SR, ST)**:
```
Specification of whether pixels that are not visible to the sensor due to terrain occlusion during off-nadir viewing.
```
INTERNAL NOTES:
ST removed the threshold ("Not required.") — the requirement is now goal-only like the SR/NLSR variant.
Confirmed: Terrain Occlusion was introduced to the ST PFS with the initial pull request (hence visible in the draft but not in the released version). ST proposes to adopt the consistent wording proposed here.

## Slide 49
Solar and Viewing Geometry (AR, SR, ST)
PFS | Current Threshold Description | Proposed Threshold Description
AR, ST (baseline) | Specification of the solar and sensor viewing azimuth and zenith angles. | (keep as is)
SR | Specification of thProvide average solar and sensor viewing azimuth and zenith angles. | Provide averagSpecification of the solar and sensor viewing azimuth and zenith angles.
PFS | Current Goal Description | Proposed Goal Description
AR, ST | (not set) | Specification of the per-pixel solar and sensor viewing azimuth and zenith angles.
SR (baseline) | Provide per-pixel solar and sensor viewing azimuth and zenith angles. | ProvidSpecification of the per-pixel solar and sensor viewing azimuth and zenith angles.
Internal notes: Proposal accepted by the ST team.
Providing the angles instead of average angles would be a breaking change — the averages may be intentional, since the per-pixel requirement may already contain all angles specifically per pixel. It is unclear what the difference between non-average and per-pixel angles would be.
Remarks from the building blocks: view-angles-solar.yaml: The threshold requirement is a metadata requirement, the goal requirement is a per-pixel requirement - should this be split?
Notes: PROPOSAL:
**Threshold — description (SR, ST)**:
```
Specification of the solar and sensor viewing azimuth and zenith angles.
```
**Goal — description (SR, ST)**:
```
Specification of the per-pixel solar and sensor viewing azimuth and zenith angles.
```
INTERNAL NOTES:
Proposal accepted by the ST team.
Providing the angles instead of average angles would be a breaking change — the averages may be intentional, since the per-pixel requirement may already contain all angles specifically per pixel. It is unclear what the difference between non-average and per-pixel angles would be.

## Slide 50
DOIs
PFS | Type / Where | Text
AR / ST | general-metadata and per-pixel-metadata — appends to description | Information should be available in the metadata as a single DOI landing page, which may include links to further detailed documents and references to citable peer-reviewed algorithms or technical documentation.
SR / NLSR / ST | In individual requirements | Information on […] should be available in the metadata as a single DOI landing page […]. or Metadata contains a single DOI landing page with references to: - a citable peer-reviewed algorithm - technical documentation regarding the implementation of that algorithm
SAR | In individual requirements | […] is provided as document referenced as URL or DOI. SI traceability is achieved. or Metadata references, e.g. - a citable peer-reviewed algorithm - technical documentation regarding the algorithm used to […] is expressed as URLs or DOIs - the sources of […]
Internal notes: How to handle references (DOIs, URLs)? (see also last CEOS-ARD OG meeting)
We need to consider per-product DOI vs other references, e.g. to algorithms, which may be external to the data provider. Should we actually describe whether something needs to be a link or can some information also be provided directly in the metadata?